## Slide 2: IBM Cloud網路存取架構 與 台灣 PoP 專線服務介紹
講義與實作文件下載處

## Slide 3: Location is key Where is the traffic coming from and where is going to?
Internet
User or
Service
IBM Cloud
Location
IBM Cloud
Location
Customer
Enterprise
Location
Edge
Edge
A network flow is like a line that always has a start and an end. Remember, once you go in one direction, you must return!
Perimeter
Perimeter
Perimeter
Perimeter
Perimeter
Perimeter
CIS
&
CDN
Direct Link
Internet
VPN
Load
Balancing
PUBLIC INTERNET
PRIVATE NETWORK
PUBLIC INTERNET
PRIVATE NETWORK
Via
PUBLIC INTERNET
PRIVATE NETWORK

## Slide 4: Internet Backbone
Public Internet
Internet only
  Security: LOW!!
  Cost: Low
  Bandwidth: Low to High
  This is the most economical method to access cloud…but has trade-offs
  DDOS, Man-in-the-middle, fuzzing, etc…is all out there. Consider CIS for ingress.
  Internet Secure Gateway – Cloud Foundry Public
  Internet SSL VPN
  Security; Moderate
  Cost; Low
  Bandwidth; Low [Less than 1G]
  Recommended for management network access only
  Most common method for mgmt control
  Internet IPSec VPN [shared hardware]
  Security; Moderate
  Cost; Low
  Bandwidth; Low
  Connects back to the customer VPN router
  Usually an extension of a customer’s existing mgmt network
  IP address is NAT’d
  Internet IPSec VPN [dedicated hardware]
  Security; Moderate
  Cost; Medium
  Bandwidth; Low to High
  Security appliance is used within the IBM cloud
Internet Only
Internet + VPN
Note; The Internet is the transport for all these solutions

## Slide 5
Decision Tree for Selecting a Private Network Connection
No
Yes
Administrative
use only ?
No
Yes
1.Internet SSL over the internet
2.VPN over the internet (shared)
Allow internet attachment ?
Yes
No
3.VPN over the internet (dedicated)
Want to share NW with Multiple Clouds ?
4a.Direct Link Exchange or Connect
4b.Direct Link Dedicated
4c.Direct Link Dedicated Hosting
Want IBM Cloud Colocation ?
Yes
No

## Slide 6
Direct Link Connect 兩種架構
(1. 專線/ 跳線 2. IP VPN)
目前接入點為香港 (預計Q2接入台灣)
https://www.chief.com.tw/dispPageBox/ct.aspx?ddsPageID=CHCLOUDSERVICE&dbid=4098738328
https://www.ibm.com/tw-zh/cloud/direct-link

## Slide 9
Jack Wu
scwu@tw.ibm.com